## Slide 1: Sub-ppm ammonia detection in urban environments with carbon nanotubes gas sensors: possible strategies to enhance the sensitivity.
Rigoni Federica
1° year Phd student
federicarigoni@gmail.com
UNIVERSITY OF MILAN – CATHOLIC UNIVERSITY OF BRESCIA

## Slide 2: Carbon nanotubes
Several allotropic form of carbon, depending on its hybridization (diamond, graphite, graphene, fullerene, carbon nanotube …)
Many scientific papers start citing
“Carbon nanotubes, discovered by
Iijima in 1991 …”
Iijima produced a new allotropic form
of carbon (that he called microtubules
of graphitic carbon), using an arc-discharge
evaporation method similar to that
used for fullerene (C60) synthesis.
S. Iijima, Nature 354 (1991) 56
sp3
Tetrahedral (3D)
sp2
Trigonal (2D)
sp
Linear (1D)
d = 3 nm

## Slide 3: What are carbon nanotubes?
GRAPHENE SHEET
CARBON NANOTUBE
C hybridization sp2
Roll-up

## Slide 4
Chiral indexes (n,m)
(17,0)
zig-zag
(10,10)
armchair
(12,8)
chiral
If n-m = multiple of 3
metallic tube
otherwise
semiconductive tube
Different chiralities: different characteristics
Single-wall carbon nanotube SWNT diameter 1-3 nm
Multi-wall carbon nanotube MWNT diameter up to 100 nm
diameter ≈ nm
length ≈ µm
1D crystal

## Slide 5: Electronic properties of SWNT
Single wall carbon nanotube has diameter ≈ nm and length ≈ µm,
We can consider it as a one-dimensional crystal.
KATAURA PLOT
Density Of States in a 1D crystal
The KATAURA PLOT relates the energy of the band gaps in a carbon nanotube and its diameter (in the first-order tight binding approximation).
Kataura et al.Synthetic Metals 103 (1999) 2555
Van Hove singularities

## Slide 6: Carbon nanotubes as gas sensors
Kong et al. Science, 287 (2000) 622
BASIC IDEA:
The interaction resulting in a charge transfer between the gas molecule and the carbon nanotube causes a variation in the electrical conductance (or resistance) of the tube, detectable with an electronic system.
NO2: OXIDIZING MOLECULE
NH3: REDUCING MOLECULE
CNTs are appealing systems for extremely sensitive gas sensors for at least two reasons:
their one-dimensional nature makes them very sensitive to tiny external perturbations
huge surface-to-volume ratio

## Slide 7: Why monitoring ammonia gas?
Ammonia concentrations over one week
in Milan (data source: ARPA Lombardia)
NH3 is one of the main precursors of secondary fine particulate (PM10, PM2.5)
In urban environment:
less than 50 ppb
Our goal: to enhance the sensitivity of carbon nanotubes based gas sensors in order to detect sub-ppm concentrations of NH3.
ppm (parts per million)
ppb (parts per billion)
Hazardous substances, explosive, …
Environmental monitoring
NH3

## Slide 8: Chemiresistor gas sensor
Drop-casting
method
Dielectrophoresis
method
Alternate Current applied during the deposition
(V = 5 V ; f = 1 MHz)
Interdigitated Pt electrodes
Alumina (ceramic)substrate
SWNT bridges between electrodes
Methods of preparation
Electrical circuit
SWNT dispersed in a solution of water, NaOH, Sodium Lauryl Sulfate
1 μl
1 μl

## Slide 9: Strategies to enhance the sensitivity of a SWNT based chemiresistor
Sonication of the sample (in ultrasound bath) to reduce the film thickness
thinner the film on the substrate, better is the charge transfer from the gas molecule to the electrical contacts.
Dielectrophoresis method to align the SWNT
a method to better distribute the SWNT on the substrate is to apply an alternate current between the electrodes, during the deposition. In this way SWNTs tends to be aligned
Functionalization
Other architectures
(e.g. chem-FET)
Moscatello et al. MRS, 1057 (2008)

## Slide 10: Response: variation of the resistance
SENSITIVITY:
sub-
ppm

## Slide 11: Dielectrophoresis method to align the CNT
Drop-casting method
Dielectrophoresis method
SEM
images
1 μl
1 μl

## Slide 12
(a) ,(b) SWNT on ceramic ID substrate

## Slide 13: In literature…
Functionalization with metal nanoparticles
High temperature
Functionalization with Polyaniline
(PANI, a conductive polymer)
There are many works on carbon nanotubes as ammonia gas sensors, but very few of them report the detection of concentrations below the ppm level.
Penza et al. Sens. And Act. B, 135(2008) 289
Zhang et al. Electroanalysis, 18 (2006) 1153

## Slide 14: Future steps
Functionalization
Different device concepts, e.g. chemical Field Effect Transistor (chem-FET)
GATE: p-doped Si
CNTs
SiO2
Source
Drain
The gate allows to change the voltage (gate voltage Vg).
S
D

## Slide 15: Chemical Field Effect Transistor (FET)
K. Uchida et al., Phys. Rev. B 79, 85402 (2009)
Vgate = 0
Vgate > 0
more electrons
Vgate < 0
more holes

## Slide 16: Thanks for the attention! QUESTIONS?

## Slide 17: Chemical Field Effect Transistor (FET)

## Slide 18: Chemical Field Effect Transistor (FET)
GATE: p-doped Si
SWNTs
S
D
Vgate > 0
Vgate = 0
Vgate < 0

## Slide 19: Experimental set-up
Commercial sensor
Based on metal oxides
Chem FET
Chemiresistor:
SWNT on interdigitated electrodes
Humidity sensor
Temperature sensor

## Slide 20: Electrical circuit
Chemiresistor
Chem-FET

## Slide 21: Raman

## Slide 22: Raman spectrum of SWNT
R. Graupner J. Raman Spectrosc. 38, 673 (2007)
Principal peaks:
RBM: Radial Breathing Mode
(150 - 350 cm¯¹)
D-band: Disorder induced band
(1350 cm¯¹)
G-band: tangential (derived from the graphite like in-plane) mode
(1560 – 1600 cm¯¹)
G’-band: overtone of D-band
Raman spectrum gives us many information about the vibrational modes of carbon nanotubes.
Raman shift (cm¯¹)
Intensity
RBM
D-band
G-band
G’-band

## Slide 23: Metallic vs Semiconductive SWNTs
L. Alvarez et al. Chem. Phys. Lett. 316, 186 (2000)
S
S
M
S
Raman spectra of SWNTs in bundles using different excitation energy (2.54, 2.41 and 1.92 eV).
The metallic or semiconducting character of the tubes is definitely confirmed by the line-shape of the TM (G-band).
G-band
RBM
Lorentian profile
Breit-Wigner-Fano
profile
semicond.
metallic
Lorentian profile
semicond.